6.pielikums

Atklāta konkursa

Nr. LiepU 2011/1 nolikumam

SPECIFIKĀCIJA - PIEDĀVĀJUMS

4.daļa Foto aparatūra, aprīkojums un materiāli

(projekts LV0063)

| N.p.k. | Specifikācija | Skaits | Garantijas laiks (gadi) | Bojājuma novēršanas laiks (stundās) | Pretendenta piedāvājums* | Vienības izmaksas** LVL | Kopējā summa LVL |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 4.1.ANALOGIE FOTOAPARĀTI NIKON N80 QD 35mm SLR Camera vai ekvivalents līdzvērtīgs |  |  |  |  |  |
| Type of camera Integral-motor autofocus 35mm single-lens reflex with electronically controlled focal-plane shutter Exposure modes Programmed Auto (Flexible Program possible™); Shutter-Priority Auto; Aperture-Priority Auto; Manual Picture Format 24mm x 36mm (standard 35mm film format) Lens mount Nikon F mount (with AF coupling, AF contacts) Compatible lenses Nikkor and Nikon lenses with Nikon F mount with limitations : D-type AF Nikkor (except IX-Nikkor) - Autofocus and all functions possible PC Micro-Nikkor 85mm f/2.8D - Usable in Manual exposure mode AF Nikkor other than D-type (except AF Nikkor for F3AF) - All functions except 3D Matrix Metering possible AI-P Nikkor - All functions except 3D Matrix Metering and autofocus possible IX-Nikkor - Cannot be used; Non-CPU - Usable in Manual exposure mode (exposure meter cannot be used) Electronic Rangefinder usable with lens with maximum aperture of f/5.6 or faster Diopter Adjustment -1.8 to +0.8 DP Viewfinder Eyepoint 15.5 to 20mm Focusing screen Nikon Advanced Focusing Screen with Vari-Brite focus area and On-Demand Grid Lines Finder magnification Approx. 92% Approx. 0.75x with 50mm lens set to infinity and -1.0 DP Viewfinder information Focus indications, metering system, AE lock, shutter speed, aperture, exposure mode, electronic analogue display/exposure compensation display, frame counter/exposure compensation, ready-light, multiple exposure, focus area, flash exposure compensation, focus area brackets, 12mm circle for Center-Weighted metering, On-Demand Grid Lines Reflex mirror Automatic, instant-return type Lens aperture Instant-return type, with depth-of-field preview button Autofocus TTL phase detection, Nikon Multi-CAM900 autofocus module - Detection range: EV -1 to EV 19 (ISO 100, at normal temperature). Lens Servo Single Servo AF (S), Continuous Servo AF (C), Manual focus (M) - Focus Tracking automatically status activated Focus area One of five focus areas can be selected AF Area mode Single Area AF and Dynamic AF (Dynamic AF Mode with Closest Subject Priority also available) Focus lock Focus is locked by pressing AF-L/AE-L button or lightly pressing shutter release button in Single Servo AF Metering system 10 segment 3D Matrix Metering, 75/25 Center-Weighted Metering & Spot Metering Metering range 3D Matrix Metering: EV 0-21; Center-Weighted Metering: EV 0-21; Spot Metering: EV 3-21 (at norm temp., ISO 100, 50mm f/1.4) Exposure meter coupling CPU and AI combined Exposure compensation Exposure compensated in �3 EV range, in 1/2 steps Auto Exposure Lock Detected exposure value locked by pressing AF-L/AE-L button Auto Exposure: Two or three frames, 1/2 steps Film speed setting DX or manual selectable: Film speed range: DX: ISO 25-5000, Manual: ISO 6-6400 in 1/3 steps Shutter Electronically controlled vertical-travel focal-plane shutter Shutter speeds 30 seconds to 1/4000 of second. plus Bulb Additional controls 18 user programmable Custom Settings Sync contact X-contact only; flash synchronization up to 1/125 sec. Built-in TTL Speedlight Guide number: 39 (ISO 100, ft) flash coverage: 28mm or longer lens; Red-Eye Reduction, TTL flash control including 3D Multi-Sensor Balanced Fill-Flash, Slow Sync and Rear-Curtain Sync are possible Flash control 5-segment TTL Multi Sensor w/ 3D Multi-Sensor Balanced Fill-Flash with built-in Speedlight, SB-28DX, SB-28, SB-27, SB-26, SB-25 Monitor Pre-flash Built-in TTL Speedlight or Nikon Speedlight SB-28DX/28/SB-27 fires Monitor Pre-flash(es) when AF Nikkor or AI-P Nikkor lens is used Flash sync mode Front-Curtain Sync (normal sync), Red-Eye Reduction, Red-Eye Reduction with Slow Sync, Slow Sync, Rear-Curtain Sync Ready-light Lights up when flash fully charged with built-in Speedlight and SB-28DX, 28, etc.; blinks (3 sec. after flash) for full output warning Accessory shoe Standard ISO-type hot-shoe Self-timer Electronically controlled; timer duration: 2 to 20 seconds with Custom Setting. DOF preview button Stops down lens aperture when pressed Film loading Film automatically advances to first frame when shutter release button is pressed once (shutter and mirror not activated) Film advance Automatic advance with built-in motor; S (Single) or C (Continuous) modes available Film advance speed S: One frame advance - C: Continuous shooting; Approx. 2.5 fps (AA-type alkaline batteries) Film rewind Auto rewind with built-in motor. Rewind speed with 36-exp. film: approx. 15 sec. Quiet rewind mode speed approx. 23 sec. Multiple exposure Activated using film advance mode dial LCD panel information (with built-in illuminator) DX indication, shutter speed/exposure compensation value, aperture, exposure compensation, Auto Exposure/Flash Exposure Bracketing, Bracketing bar graphs, Custom, Flexible Program, flash sync mode, AF area mode, focus area, battery power, frame counter Power source Two CR123A batteries Exposure meter Auto meter shut-off approx. 6 sec. Usable number of film rolls (approximate) With 36-exposure film, for Continuous Servo autofocus operation using an AF Zoom-Nikkor 28-80mmf/4-5.6D lens, in single-frame shooting, covering the full range from infinity to the closest distance and back to infinity before each shot, without intervals between shots, with a shutter speed of 1/125th sec. or faster. Dimensions (W x H x D) Approx. 141.5 x 98.5 x 71 mm ( 5.6 x 3.9 x 2.8 in.) Weight (without batteries) Approx. 515g (18.2 oz) | 6 | 2 | 48 |  |  |  |
| 4.2.OBJEKTĪVI Nikon 50mm f/1.8D AF Nikkor Lens vai ekvivalents līdzvērtīgs |  |  |  |  |  |
| Nikon 50mm f/1.8D AF Nikkor Lens Mount Type: Nikon F-Bayonet Focal Length: 50mm Maximum Aperture f/1.4 Minimum Aperture f/16 Maximum Angle of View (DX-format) 31°30' Maximum Angle of View (FX-format) 46° Maximum Reproduction Ratio 0.15x Lens (Elements) 7 Lens (Groups) 6 Compatible Format(s) FX DX FX in DX Crop Mode 35mm Film Diaphragm Blades 7 Distance Information Yes Super Integrated Coating Yes Autofocus Yes Minimum Focus Distance 1.5ft.(0.45m) Focus Mode Auto, Manual Filter Size 52mm Accepts Filter Type Screw-on Dimensions (Approx.)2.5x1.7 in. (Diameter x Length) 64.5x42.5mm (Diameter x Length) Weight (Approx.)8.1 oz. (230g) Supplied Accessories 52mm lens cap Rear lens cap | 6 | 2 | 48 |  |  |  |
| 4.3.FILTRI Sigma DG 52mm Multi-Coated UV Filter vai ekvivalents līdzvērtīgs |  |  |  |  |  |
| Vidēji dzeltens 52 mm | 6 | 2 | 48 |  |  |  |
| Vidēji oranžs 52 mm | 6 | 2 | 48 |  |  |  |
| 4.4.TĪRĪŠANAS SLOTIŅAS Hama Lens Cleaning Pen vai ekvivalents līdzvērtīgs |  |  |  |  |  |
| Double-Ended Brush and Velvet Pad 23 x 9 x 2.5 cm | 8 | 2 | 48 |  |  |  |
| 4.5.STATĪVI Bowens BW-6610 BLACK COMPACT STAND (Max height 303cm Closed 87cm) vai ekvivalents līdzvērtīgs |  |  |  |  |  |
| Primary material – Aluminium Colour – Black Weight (g) – 1700 Min height - 83cm Max height - 303 cm Size - 86cm Closed | 2 | 2 | 48 |  |  |  |
| 4.6.LIETUSSARGS Bowens RD-4046 Lietussargs 115 cm (46”) ar pārvelkamu virsmu sudraba/melns vai ekvivalents līdzvērtīgs |  |  |  |  |  |
| Type – Umbrella For use with - Studio Flash Heads - (8mm Shaft) Colour – Silver/White Removable exterior - Yes Size - 115cm Weight (g) – 500 | 2 | 2 | 48 |  |  |  |
| 4.7.ZIBSPULDZE I Nikon SB-600 Speedlight vai ekvivalents līdzvērtīgs |  |  |  |  |  |
| Nikon SB-600 Speedlight Flash exposure control • i-TTL • D-TTL • TTL (film based) • Balanced fill-flash • Manual Guide number • 30/98 (ISO 100, m/ft) • 42/138 (ISO 200, m/ft) * at 35 mm zoom-head position, 20°C / 60°F Flash coverage • 24 - 85 mm • Extendable to 14 mm with built-in wide-flash adapter • Manual Flash shooting distance range • 0.6 to 20 m (2 to 65.6 ft) * in auto flash mode, varies depending on ISO, zoom-head position and lens aperture Power switch • Off • Standby Recycling time • Approx. 3.5 sec (Alkaline battery) Number of flashes • Approx. 200 (Alkaline battery) Creative lighting system A variety of flash operations are available with camera's compatible with CLS: i-TTL mode, Advanced Wireless Lighting, FV Lock flash, Flash color information communication, Auto FP High-Speed sync, Wide-area AF-Assist Illuminator. Display LCD segment type LCD back light LED type Shoe-lock One action lock Power 4 x AA batteries Dimensions 124 x 90 x 68 mm (4.9 x 3.5 x 2.7 in) s Weight (no batt) 300g (9.6 oz) Box contents Speedlight stand (AS-19), Soft case (SS-600), SJ-1 Colour filter set included | 2 | 2 | 48 |  |  |  |
| 4.8.ZIBSPULDZE II Nikon SB 900 vai ekvivalents līdzvērtīgs |  |  |  |  |  |
| Electronic construction | Automatic Insulated Gate Bipolar Transistor (IGBT) and series circuitry | 1 | 2 | 48 |  |  |  |
| Guide number (20°C/68°F) | 34/111.5 (ISO 100, m/ft), 48/157.5 (ISO 200, m/ft) |  |  |  |  |  |  |
| Illumination pattern | Three illumination patterns: standard, even and center-weighted The light distribution angle is automatically adjusted to the camera's image area in both FX and DX formats |  |  |  |  |  |  |
| Flash shooting distance range | 0.6 m to 20 m (2 to 66 ft) (varies depending on camera image area setting, illumination pattern, ISO sensitivity, zoom position, and lens aperture) |  |  |  |  |  |  |
| Flash mode | TTL, Auto Aperture flash, Non-TTL auto flash, Distance-priority manual flash, Manual flash, Repeating flash |  |  |  |  |  |  |
| Other functions | Test firing, monitor pre-flashes, AF-assist illuminator, and Modeling illuminator |  |  |  |  |  |  |
| Multiple flash operation | Advanced Wireless Lighting, SU-4 type wireless multiple flash |  |  |  |  |  |  |
| Compatible cameras | All cameras compatible with Nikon Creative Lighting System (other cameras can be used but functionality is reduced) |  |  |  |  |  |  |
| Flash exposure control set on the camera | Camera's sync modes: Slow-sync, Red-eye reduction in slow-sync, Rear-curtain sync, Rear-curtain slow-sync |  |  |  |  |  |  |
| Bounce capability | Flash head tilts down to -7° or up to 90° with click-stops at -7°, 0°, 45°, 60°, 75°, 90° Flash head rotates horizontally 180° to the left and right with click-stops at 0°, 30°, 60°, 90°, 120°, 150°, 180° |  |  |  |  |  |  |
| Power source | Four AA-size alkaline-manganese (1.5V), lithium (1.5V), Oxyride (1.5V) or Ni-MH (2600 mAh) (rechargeable) (1.2V) batteries |  |  |  |  |  |  |
| Ready light | The SB-900 is fully recycled: Rear ready-light lights up and front light blinks Insufficient light for correct exposure (in i-TTL, Auto Aperture flash, Non-TTL Auto flash, or Distance-priority manual flash operations): ready-lights and front lights blink after shooting |  |  |  |  |  |  |
| Flash duration | Approx. 1/880 sec. at full output |  |  |  |  |  |  |
| Mounting foot lock lever | Provides secure attachment of SB-900 to camera's accessory shoe using locking plate and mount pin to prevent accidental detachment |  |  |  |  |  |  |
| Dimensions (W x H x D) | Approx. 78.0 x146.0 x 118.5 mm (3.0 x 5.7 x 4.7 in.) |  |  |  |  |  |  |
| Weight (without batteries) | Approx. 415 g (14.6 oz.) |  |  |  |  |  |  |
| Supplied accessories | Speedlight Stand AS-21, Nikon Diffusion Dome SW-13H, Color Filter Set SJ-900, Color Filter Holder SZ-2, Soft Case SS-900 |  |  |  |  |  |  |
| 4.9.EKSPONOMETRS Seconic 308B vai ekvivalents līdzvērtīgs |  |  |  |  |  |
| Izmēri, mm 110х63х22 Barošanas veids 1x AA Tips Kompaktais digitālais eksponometrs impulsa un pastāvīga apgaismojuma mērīšanai Exposures accurate down to a tenth-of-a-stop for both ambient and electronic flash light readings in full-stop mode. Meter can also display shutter-speeds and apertures in half or third-stop increments to mirror the exposure settings on your camera with a repeat accuracy of +/- 0.1 EV At ISO 100, the ambient EV range is 0 to 19.9, flash f/stops range from f/1.4 to f/90.9 with a shutter-speed span of 60-seconds to 1/8000th-of-a-second (1 sec to 1/500th for flash). For cinema applications frame rates can be set from 8 to 128 frames-per-second. ISO sensitivity can be set from 3 to 8000 in third-stop increments | 2 | 2 | 48 |  |  |  |
| 4.10.SOFTBOKS Walimex Magic Square Softbox ar statīvu vai ekvivalents līdzvērtīgs |  |  |  |  |  |
| Dimension softbox approx. 40x40cm Depth softbox approx. 40cm Carrying dimension approx. 45x44x9cm Connection 5/8 inch spigot Tripod: Max. height approx. 200cm Carrying length approx. 81cm Weight approx. 1040g Max. load capacity approx. 2500g Connection 5/8 inch spigot with 1/4 inch screw Material aluminium | 1 | 2 | 48 |  |  |  |
| 4.11.PIEDERUMI |  |  |  |  |  |
| 4.11.1.Fotolaboratorijas piederumu komplekts – pozīcijas ar skaitu |  |  |  |  |  |
| Delta Junior 11 Watt Universal red fotolaboratorijas spuldzes, 12 gab. Kaiser fotolaboratorijas lampa (sarkanais, zaļais filtrs) Kalt Mērtrauki, 2 gab Hama filmu kasešu attaisāmais, 1 gab Jobo knaģi filmu žāvēšanai (12 gab.) Jobo liekā ūdens notrausējs (filmām), 2 gab AP lupa 8x; AP filmas gala izvilcējs no kasetes; Kaiser laboratorijas vanniņa 24x30 sarkana, 6 gab. (3 dziļās, 3 seklās) Kaiser laboratorijas vanniņa 30x40 sarkana, 4 gab (2 dziļās, 2 seklās) Kaiser plastmasas pincetes, 4 gab Kaiser kolbu termometrs, 1 gab Kaiser vanniņu termometrs, 1 gab Kaiser ķimikāliju pudele 1000ml, 3 gab Kaiser piltuve 120mm, 1 gab Kaiser plastmasas pincetes ,4 gab Jobo tanki 1520, divstāvīgie, ar spolēm, 2 gab Jobo tanki 1510, vienstāvīgie, ar spolēm, 2 gab Kaiser hronometrs "digital", 1 gab |  |  |  |  |  |  |
| 4.11.2.SOMAS |  |  |  |  |  |
|  | Lowepro Rezo 160 Shoulder Bag For Digital SLR – Black Product Dimensions: 23.9 x 21.3 x 14.5 cm ; 490 g Boxed-product Weight: 908 g | 6 | 2 |  |  |  |  |
| 4.11.3.APGAISMOJUMA KOMPLEKTS |  |  |  |  |  |
| Elinchrom D-Lite 4 vai ekvivalents līdzvērtīgs |  |  |  |  |  |  |
| Power: 400Ws No of f/stops: 5 Power range: 25 - 400Ws Power adjustment: 1/10stop steps f/stop at 1m: f/64.3 Recycling time 1.3s -0.4s Flash duration @ 0.5: 1/800sec Power stabilisation 0.5% Power discharge: Auto Modelling lamp: 100W / E27 Modelling lamp setting: Prop, half, on and off Flashtube: User replacement No 24009 Umbrella fitting: 7mm diameter Sync voltage (VDC) 5V (okay with digital cameras) Sync socket: 3.5mm jack Temperature protection: Yes Over-voltage protection: Yes Dimension: 21cm length x 16cm diameter Weight: 1.3 kg Included: 1× ELS Transmitter ECO (19349), 2× D-Lite-it 4 (20484.1), 1× Tripod Set 2 (30162), 2× Portalite Softbox (26129), 1× Umbrella Wide Reflector 90° 16 cm (26143), 1× Protective Hood (26124), 1× Tube Bag - Compacts (33198) | 1 kompl |  |  |  |  |  |
| 4.11.3.Ķīmija un papīrs (derīguma termiņš vismaz 5 gadi no piegādes brīža): |  |  |  |  |  |
|  | Foto filmas: Ilford Delta 100 135-36 140 gab Ilford Delta 400 135-36 140 gab Filmu attīstītājs: Ilford Ilfotec DD-X 1 + 4 14 litri Ilford fotopapīri – Multigrade Paper RC Base Delux MGIV RC Delux 17.8 x 24 1400 loksnes MGIV RC Delux 24 x 30.5 700 loksnes MGIV RC Delux 30.5 x 40.6 850 loksnes Ķīmija papīra apstrādāšanai - attīstītājs Ilford Multigrade 70 litri fiksāža Ilford Rapid Fixer 14 litri MACO ecostop 14 litri |  |  |  |  |  |  |
|  | KOPĀ |  |
|  | 22%PVN |  |
|  | Pavisam kopā |  |

* ja piedāvājuma parametri sakrīt ar pieprasījuma parametriem, atzīmēt ar X, ja parametri atšķirīgi, norādīt precīzu informāciju

**-Ietverot iekārtu piegādes izmaksas, iekārtu uzstādīšanas izmaksas un lietotāja pamata apmācības izmaksas.