8.pielikums

Atklāta konkursa

Nr. LiepU 2011/1 nolikumam

SPECIFIKĀCIJA - PIEDĀVĀJUMS

6.daļa Skaņas aparatūra, aprīkojums un piederumi

| N.p.k. | Specifikācija | Skaits | Garantijas laiks (gadi) | Bojājuma novēršanas laiks (stundās) | Pretendenta piedāvājums* | Vienības izmaksas** LVL | Kopējā summa LVL |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 6.1.Skaņas aparatūra, aprīkojums un piederumi (projekts LV0063) |  |  |  |  |
| 6.1.1. Universāla audio ierakstu darbstacija LA-610 MKII vai ekvivalents līdzvērtīgs |  |  |  |  |  |
| Mic, Line and Hi-Z Input, Line Output Dual Impedance Mic and Hi-Z inputs (Mic: 2K, 500Ω, Hi-Z: 2.2M, 47KΩ) 5 position Stepped Preamp Input Gain, Continuous Preamp Output Level -15dB Pad Switch (15dB Pad/Off) Phase reverse (0/180º) 48 volt Phantom Power switch (+48v/Off) +/- 9 dB stepped High Shelving Filter (4.5, 7, 10 kHz) +/- 9 dB stepped Low Shelving Filter (70, 100, 200 Hz) T4 Optical Compressor with Continuous Peak Reduction and Makeup Gain Compress/Limit/Bypass Modes of Dynamic Operation (3:1 / ∞: 1) Meter Source Selector Switch (Preamp/Gain Reduction/Compressor) Front Panel Power switch (On/Off) Custom Altran and Cinemag Transformers Microphone Input Impedance: Selectable, 500 Ohms or 2k Ohms Balanced Line Input Impedance: 20k Ohms Hi-Z Input Impedance: Selectable, 2.2M Ohms or 47k Ohms Maximum Microphone Input Level: -8 dBu (2K input Imp. & 15 dB Pad in) Maximum Output Level: 80 Ohms Recommended Minimum Load: 600 Ohms Frequency Response: 20 Hz to 20 kHz ± 0.5dB Maximum Gain: 40 dB (Line), +77dB (Mic) Noise Floor: -72 dBu 20 - 20kHz (Line In, unity Gain) Compressor Ratio: 3:1, soft knee, program dependent Limiter Ratio: ∞: 1, soft knee, program dependent Attack Time: 10 ms, program dependent Releas Time: Dual stage: 60 ms for 1st release, then 1 - 15 sec. Tube Complement: (3) 12AX7, (1) 12AT7, (1) EL84 | 1 | 2 | 48 |  |  |  |
| 6.1.2.Profesionālas stereo austiņas studijas un raidījumu ierakstu lietošanā AKG 141 Mk II vai ekvivalents līdzvērtīgs |  |  |  |  |  |
|  | Type semi-open, dynamic headphones Sensitivity101 dB/mW, 114 dB/V Frequency range18 to 24,000 Hz Rated impedance55 ohms Max. input power200 mW Studio monitors Genelec 8050 A Technical Specifications Input format Analog SPL Maximum short time sine wave acoustic output at 1 m on axis in half space, averaged from 100 Hz to 3 kHz ≥ 110 dB SPL Maximum peak acoustic output per pair with music material ≥ 120 dB SPL @ 1m Drivers Bass 8" Treble 1" metal dome Crossover frequencies 1.8 kHz Free field frequency response 38 Hz - 20 kHz Amplifier power /ch Bass 150 W Treble 120 W Speaker dimensions (H x W x D) mm 433 x 286 x 278 mm (Height with Iso-Pod™ 452 mm) | 1 | 2 | 48 |  |  |  |
| 6.1.3.Savietojams sistēmā ar esošo Genelec 8050 A monitoru un pastiprinātāju skaļruni Genelec 7070 A vai ekvivalents līdzvērtīgs |  |  |  |  |  |
|  | 1 | 2 | 48 |  |  |  |
| 6.1.4.FireWire audio interfaiss (saskarne) Apogee Duet vai ekvivalents līdzvērtīgs |  |  |  |  |  |
|  | Two channels of professional-quality 24-bit/96kHz audio input and output Two balanced XLR inputs, with selectable 48V phantom power on each input Maximum input - +4 dBu setting: 20 dBu; -10 dBV setting: +8 dBV Mic Pre-amp gain: 10 to 75 dB Two unbalanced high impedance instrument inputs One high-level stereo headphone output Two unbalanced -10 dBV line outputs for powered speakers Multi-function controller knob for volume and input gain control Multi-segment LED meters to display input or output levels | 1 | 2 | 48 |  |  |  |
| 6.1.5.Pastiprinātājskaļrunis Dyanaudio BM 14S vai ekvivalents līdzvērtīgs |  |  |  |  |  |
|  | System - Active Subwoofer Frequency Response (+/- 3 dB) 18 Hz - 250 Hz Sub input, 18 Hz - 250 Hz LFE input Low Frequency Limit 18 Hz High Frequency Limit 50 Hz - 250 Hz Sub input, 150 Hz LFE input Amplifier Power 300 W @ 4 Ohms Crossover Frequencies HP Sat: Flat / 60 Hz / 80 Hz Low Pass filter 50 – 150 Hz | 1 | 2 | 48 |  |  |  |
| 6.1.6.Austiņu pastiprinātājs Preonus HP 60 vai ekvivalents līdzvērtīgs |  |  |  |  |  |
|  | Six independent ultra low noise, high output headphone amplifiers (150 mW per channel) Two sets of stereo inputs (A and B) with balanced TRS connectors Stereo external input point on each channel for “more me” with trim control Mix control between inputs A and B Talkback with external XLR microphone with control Direct stereo line output on each channel | 1 | 2 | 48 |  |  |  |
| 6.1.7.Aktīvā skaļruņu sistēma KV2 Audio EX12 vai ekvivalents līdzvērtīgs |  |  |  |  |  |
|  | System acoustic performance –3dB response 55Hz - 20KHz –10dB response 50Hz - 20KHz Max SPL long-term 127dB Max SPL Peak 130dB High Frequency Section Throat Exit Diameter/ Diaphragm Size 1.4" / 3" Diaphragm Material Nitride Titanium Magnet Type Neodymium Horn with Constant Directivity Coverage Horizontal/ Vertical 80° x 40° Low Frequency Section Acoustic Design Front Loaded, Bass Reflex Woofer Size/ Voice Coil Diameter/ Design 12" / 2.5" / Trans Coil Diaphragm Material Epoxy Reinforced Cellulose Magnet Type Neodymium High Frequency Amplifier Type Class AB Push-Pull Rated Continuous Power 50W Distortion <0.05% Operating Bandwidth 1.1kHz - 30kHz Bass Amplifier Specification Type High Efficiency Switching Rated Continuous Power 450W Distortion <0.05% Operating Bandwidth 45Hz - 1.1kHz | 1 | 2 | 48 |  |  |  |
| 6.1.8.Aktīvā skaļruņu pastipronātājsistēma KV2 Audio EX1,2 vai ekvivalents līdzvērtīgs |  |  |  |  |  |
|  | System Acoustic Perfomance -3dB Response 38Hz - 120Hz -10dB Response 32Hz - 120Hz Max. SPL Long-term 124dB Max. SPL Peak 127dB Crossover Point 120Hz Low Frequency Section Acoustic Design Twin Asymmetrical loading Woofer size / Voice Coil Diameter / Design 12" / 3" / Inside outside Diaphragm Material Epoxy Reinforced Cellulose Magent Type Neodymium Bass Amplifier Specification Type High Efficiency Switching Rated Continuous Power 500W Distortion <0.05% | 1 | 2 | 48 |  |  |  |
| 6.1.9. MOTU atskaņotājs MkIII vai ekvivalents līdzvērtīgs |  |  |  |  |  |
| Four 24-bit 192 kHz mic/guitar inputs A-weighted dynamic range 120dB THD+N of 0.00056% (-106dB) Compact size (14.75 x 9 inches) Powered via FireWire, Optional battery power via standard field battery pack (sold separately) 28 inputs / 30 outputs (at 44.1/48 kHz) Four combo jacks provide hi-Z 1/4" guitar input or low-Z XLR mic input with phantom power and pad, Clip protection - Up to +12 dB over zero, Individual 48V phantom power on each mic input Four 24-bit 192kHz analog inputs and eight analog outputs on balanced/unbalanced 1/4" TRS jacks optical I/O - 16 channels of ADAT lightpipe, 8 channels of SMUX (96 kHz) or two pairs of stereo TOSLink. Eight 24-bit 192kHz outputs on balanced/unbalanced 1/4" TRS jacks. Stereo 24-bit 96kHz AES/EBU in/out Stereo 24-bit 96kHz S/PDIF in/out Word clock in and out Built-in SMPTE time code sync - resolves to and generates time code Input Output Analog 24-bit 192-kHz on +4/-10 bal/unbal TRS 4 8 Mic preamps 24-bit 192-kHz on XLR/TRS combo 4 - Headphone output* - stereo ADAT optical (digital)† 16 16 S/PDIF 24-bit 96-kHz (digital) stereo stereo AES/EBU 24-bit 96-kHz (digital) stereo stereo Total 28 30 # Powered by computer* — no additional power supply necessary for complete recording freedom. # Optional battery power — standard field battery pack (sold separately) can be used for extended remote recording sessions and stand-alone operation as a complete digital mixer. # 28 inputs / 30 outputs (at 44.1/48 kHz) — there's no channel sharing in the Traveler-mk3. Mic inputs, TRS analog, AES/EBU, RCA S/PDIF and phones are all handled as separate channels. # Four combo jacks provide hi-Z 1/4” guitar input or low-Z XLR mic input with transparent preamps, phantom power, pad and plenty of gain. # Clip protection — Mic/guitar input limiter prevents digital clipping and distortion from overloaded signal levels up to +12 dB over zero. # Individual 48V phantom power on each mic input — mix and match microphones. # Four 24-bit 192kHz analog inputs and eight analog outputs on balanced/unbalanced 1/4" TRS jacks. # Digital Precision Trim™ — adjust input gain in 1dB increments on all analog inputs (mic/guitar inputs + quarter-inch TRS inputs). Fine-tune the balance of your analog inputs. Save and recall multiple trim setups. # High-resolution recording — The Traveler-mk3 can operate all analog I/O at sample rates up to 192kHz. # Flexible optical I/O — 16 channels of ADAT lightpipe, 8 channels of SMUX (96 kHz) or two pairs of stereo TOSLink. Mix and match formats between the two banks. # CueMix FX™ — flexible 28 input/16 bus mixer with on-board DSP effects, including classic reverb with sends/returns, plus modeled EQ and vintage compression on every input and output. # Multiple CueMix FX mixes — for example, create different monitor mixes for the main outs and headphones. Or add send/return loops for outboard gear with no latency. # Advanced audio signal analysis — CueMix FX software provides real-time FFT and spectrogram "waterfall" displays for visual analysis of individual signals and entire mixes. # Front-panel control — access your entire mix, or any Traveler-mk3 setting, directly from the front panel. # Stand-alone operation — program your mixes at the studio and then bring the Traveler-mk3 to your gig — no computer needed. Just plug in the included DC power adapter. Tweak settings using the back-lit LCD. # Sample-accurate MIDI — connect a MIDI controller and/or sound module with no separate interface needed. MIDI I/O is sample-accurate with supporting software. # Expandable — add additional interfaces for more I/O as your needs grow. # Compatible with the 8pre mic input expander — connect the 8pre via optical for 8 more mic inputs at sample rates up to 96 kHz fully integrated into the Traveler-mk3's CueMix FX mixing environment. # Eight 24-bit 192kHz outputs on balanced/unbalanced 1/4" TRS jacks. # Phone jack with front panel volume control. # Stereo 24-bit 96kHz AES/EBU in/out. # Stereo 24-bit 96kHz S/PDIF in/out. # Word clock in and out. # Built-in SMPTE time code sync — resolves to and generates time code. Allows you to directly resolve Digital Performer, Logic, Cubase, Nuendo and other compatible host software to time code with no additional synchronizer needed. # Plug-and-play operation with your Mac or PC via FireWire. # Includes drivers for Mac OS X and Windows XP/Vista, including ASIO, WDM, Core Audio, and Core MIDI. # Supports all popular Mac and Windows audio software. # 100% compatible with all host-based effects processing in today's popular audio programs. # Includes AudioDesk 3 full-featured sample-accurate workstation software for the Mac OS X with recording, editing, mixing, real-time 32-bit effects processing & sample-accurate sync. # Plug-and-play operation with your Mac or PC via FireWire — Two FireWire 400 ports allow for daisy-chaining without a hub. Works with a FireWire 800 connection via a simple adapter or FW400-to-800 cable. # Front panel volume control for monitoring. Stereo, Quad, 5.1, 7.1 and user-defined surround monitoring setups available. # Front panel meters or activity LEDs for all analog, digital and MIDI I/O, plus SMPTE sync, tach and lock LEDs. # Comprehensive level metering — Front panel LCD provides vertical meters for entire banks (8 channels at once) or horizontal long-throw metering for individual channels. Meter banks are quickly accessible via the dedicated METERS rotary encoder on the front panel. # Dedicated front panel clock status LEDs. # Chassis dimensions, excluding rack ears and front and back panel knobs and connectors: 14.75 x 9 x 1.75 inches (37.47 x 22.86 x 4.45 cm). Knobs and connectors extend up to 0.5 inch (1.27 cm) from front and back panels, adding 1 inch (2.54 cm) to depth. With rack ears attached, fits standard 19 inch (48.26 cm) rack at 1U high. | 1 | 2 | 48 |  |  |  |
| 6.1.10. Īpatnēja tembra Mikrofons solo balss un solo instrumentu ierakstīšanai AKG C 414 XL II/ST vai ekvivalents līdzvērtīgs |  |  |  |  |  |
|  | Stereo set of two C 414 XL II Polar pattern Omnidirectional, wide cardioid, cardioid, hypercardioid, figure eight and 4 intermediate settings Frequency range 20 to 20,000 Hz Sensitivity 20 mV/Pa (-34 dBV) ± 0.5 dB Max. SPL 200/400/800/1600 Pa = 140/146/152/158 dB (0/-6/-12/-18 dB) for 0.5% THD Equivalent noise level 6 dB-A (0 dB preattenuation) (IEC 60268-4) Signal/noise ratio (A-weighted) 88 dB Preattenuation pad 0 dB, -6 dB, -12 dB, -18 dB, switchable Bass cut filter slope 12 dB/octave at 40 Hz and 80 Hz; 6 dB/octave at 160 Hz Impedance <=200 ohms Recommended load impedance >= 2,200 ohms Supply voltage 48 V phantom power to DIN/IEC Powering approximately 4 mA Connector 3-pin XLR to IEC Finish dark grey/gold Dimensions 50 x 38 x 160 mm (2.0 x 1.5 x 6.3 in.) Net weight 300 g (10.6 oz.) Patent(s) Electrostatic transducer (Patent no. AT 395.225, DE 4.103.784, JP 2.815.488) | 1 | 2 | 48 |  |  |  |
| 6.1.11. Dubultmikrofonu paliktnis AKG H 50 Stereo Bar vai ekvivalents līdzvērtīgs |  |  |  |  |  |
|  | for Mounting Two Microphones C 414 XL II | 1 | 2 | 48 |  |  |  |
| 6.1.12. 4 mikrofonu statnis K&M 21021 vai ekvivalents līdzvērtīgs |  |  |  |  |  |
|  | Overhead microphone stand - extra high stand with long boom and wide feet, height: 1120-2010mm, boom length: 1065mm. Weight: 5.84kg. Colour: Black. | 1 | 2 | 48 |  |  |  |
| 6.1.13. Analogs moduļu sintezators Doepfer A-100BS2 Basis-System 2,230 V vai ekvivalents līdzvērtīgs |  |  |  |  |  |
|  | Komplektācija: * 2x Standard VCO A-110 * 2x ADSR A-140 * 2 x LFO A-145 * 1x Ring Modulator A-114 * 1 x Audio Divider A-115 * 1 x VC Waveform Processor A-116 * 1 x Noise/Random A-118 * 1 x VCF1 A-120 (24dB low pass 1) * 1 x VCF2 A-121 (12dB multimode filter) Remark: Module A-121 will be placed in the basic systems from January 2010 by the A-106-6 XP Filter. The production of the A-121 has to be stopped because of the no longer available special circuit CEM3320. * 1 x linear VCA A-130 * 1 x logarithmic VCA A-131 * 1 x linear Mixer A-138a * 1 x logarithmic Mixer A-138b * 1 x Dual S&H A-148 * 1 x Trigger Divider A-160 * 1 x Trigger Sequencer A-161 * 1 x Dual Slew Limiter A-170 * 1 x Multiple I A-180 * 30 patch cables (mixed) MIDI interface A-190 and a 4HP blind plate | 1 | 2 | 48 |  |  |  |
| 6.1.14. Papildus moduļi Doepfer analogajam moduļu sintezatoram vai tā ekvivalentam līdzvērtīgam |  |  |  |  |  |
|  | 2 x A-110 Standard-VCO 140,00 1 x A-114 Dual-Ringmodulator 70,00 2 x A-138a Mixer linear 45,00 2 x A-119 Ext.Input/Env.Follower 60,00 2 x A-141 VC-ADSR 100 A-176 Control Voltage Source A-178 Theremin 75,00 A-136 Distortion/Waveshaper 60,00 A-199 Spring Reverb 110,00 A-117 Digital noise 65 Casing and 30 patchcables for modules | 1 | 2 | 48 |  |  |  |
| 6.1.15. Clark Syntesis AQ Aquasonic skaļrunis vai ekvivalents līdzvērtīgs |  |  |  |  |  |
|  | Continuous Power Handling 135 watts Impedance 4 ohms Overload Protection Polyswitch Frequency Response 20Hz to 17kHz Electrical Connection 100 ft.- Underwater, 16-2 wire Dimensions 8 in. diam. x 4.5 in. (11.5 cm) deep | 1 | 2 | 48 |  |  |  |
| 6.1.16.Skaņu iekārtas 702T savienojuma pāreja digitālam ierakstītājam ar laika kodu vai ekvivalents līdzvērtīgs |  |  |  |  |  |
| * Two-channels of Sound Devices next generation microphone preamps with phantom, limiters, and high-pass filters * Records to convenient, removable Compact Flash storage * Full-function, ultra-stable Ambient time code functionality,, tuneable to <0.2 PPM accuracy with all relevant TC rates * AES3 (XLR) or AES3id (unbalanced AES on BNC) digital inputs and AES3id outputs * Programmable, sunlight-viewable LED level metering * WAV format, mono or poly files, uncompressed PCM audio * 24-bit or 16-bit (with or without dither) and sampling at 32 kHz-192 kHz * MP3/ MP2 file playback * FireWire (IEEE-1394) port for high-speed data transfer to computers * 6-pin modular C. Link serial input and output for unit linking and control and expansion using the CL-1 * Removable Li-on rechargeable battery compatible with Sony M- and L-mount Li-on batteries * 10–18 VDC external input powers and charges on-board battery * Aluminum & stainless-steel chassis for exceptional durability and light weight * Class-defining compact size * Designed for the same operational environmental extremes as Sound Devices field mixers Specifications Sampling Frequency: internal: 32, 44.1, 48, 48.048, 88.2, 96, 96.096, 176.4, 192 kHz; external: 32–192 kHz via word clock input Internal Data Path and Processing: 32 bit, 192 dB dynamic range A/D, D/A Converters: 24 bit, 192 kHz sample rate maximum A/D Dynamic Range: 114 dB, A-weighted bandwidth 110 dB, 20 Hz – 22 kHz bandwidth D/A Dynamic Range: 112 dB, A-weighted bandwidth 108 dB, 20 Hz–22 kHz bandwidth Frequency Res. Mic or Line: 10 Hz–40 kHz, +0.1, -0.5 (gain controls centered), Fs 96 kHz Equivalent Input Noise: Mic: -133 dBu max (-135 dBV), 50 ohm source, A-weighted filter Mic: -131 dBu max (-133 dBV) max, 50 ohm source, 20 Hz–20 kHz BW flat filter, gain fully up Mic: -130 dBu max (-132 dBV), 150 ohm source, A-weighted filter Mic: -128 dBu max (-130 dBV), 150 ohm source, 20 Hz–20 kHz BW flat filter, gain fully up THD + Noise: Mic: 0.004% max (1 kHz, 22 Hz–22 kHz BW, gain control down, -15 dBu input); line: 0.004% max (1 kHz, 22 Hz–22 kHz BW, gain control down, +16 dBu input) Gain: (input dBu to -20 dBFS) mic (normal gain mode): 25 to 70 dB; mic (low gain mode): 10 to 55 dB; line: -6 to 18 dB, 0.1 dB increments Input Clipping Level: Mic input: -5 dBu minimum (normal gain mode, gain control fully down); mic input: +10 dBu minimum (low gain mode, gain control fully down); line input: +26 dBu minimum (gain control fully down) High-Pass Filters: 40, 80, 160, 240 Hz @ 12/18/24 dB/oct (all menu selectable) Mic Powering: (each XLR selectable): 48 V phantom through 6.8k resistors, 10 mA per mic available, menu-selected per channel in mic or line level positions Mic Input Limiters: analog (pre-A/D converter), dual-stage optocoupler and FET, -4 dBFS threshold, 20:1 limiting ratio, 5 mS attack time, 200 mS release time Analog Line Output Clipping Level: +24 dBu minimum, 10k ohm load Attenuation & Resolution 0 to 40 dB, 1 dB increments I/O – Digital: AES3-id 75 ohm, 0.5 V p-p, S/PDIF compatible with RCA adapter Digital Storage: Compact Flash CF type I, II, and + (microdrive) compatible, FAT32 formatted, 2 TB maximum File Types WAV or BWF, mono or polyphonic; MP3 @ 64, 96, 128, 240, or 320 kb/s stereo; utilities: format, speed test, and repair utility for internal HD and CF volumes Data Transfer / Control: FireWire peripheral-mode,IEEE-1394a compliant, 6-pin FireWire, Windows 2000, XP, Mac OS X only: C. Link 6-pin modular input and output, RS-232 machine control, word clock, time code transfer Metering: 38-segment (2 x 19), sunlight-viewable, selectable peak, VU, or peak (with or without peak hold) with VU ballistics, variable brightness Time Code: modes supported: free run, record run, 24 hour run, continuous jam; frame rates 23.976, 24, 25, 29.97DF, 29.97ND, 30DF, 30ND; accuracy <0.2 ppm, when tuned with Ambient Master Controller; holds TC clock for 2 hours after main battery removal (AA time code battery installed); retains time of day Powering: operating cell, removable 7.2 V (nominal) Sony M- or L-type Li-on, operational from 6 – 8 V; time code battery, 1.2 V AA nickel metal-hydride; power supply (external) 10–18 V, 1 A minimum, via locking 4-pin Hirose connector, use Hirose #HR10-7P-4P (DigiKey# HR100-ND) for locking mating DC connector; pin-4 = (+), pin-1 = (-) or pin-3 = (+) and pin-2=(-). Environmental: operation and storage: ambient temperature 5–55° C, relative humidity (non-condensing) <80% Other: LCD Display 202 x 32 pixel, extended temperature, backlit display; tone oscillator 100 Hz–10 kHz, variable output, assigned to tracks or outputs (menu-selectable); Dimensions and Weight: 45 mm x 209 mm x 125 mm (H x W x D) 1.8” x 8.2” x 4.9” mass unpackaged: 1.0 kg, (2.1 lbs) without battery | 1 | 2 | 48 |  |  |  |
| 6.1.17.Universālie diafragmas kondensatoru mikrofonu saskaņotais stereo pāris Rode NT5 vai ekvivalents līdzvērtīgs |  |  |  |  |  |
|  | Compact 1/2" small-diaphragm Cardioid Condenser Microphone * Externally biased condenser * Gold sputtered 1/2" capsule * Heavy-duty satin-nickel plated body * Surface mount circuitry * Low noise * Full frequency response Power P48 (48V), P24 (24V) phantom supply Acoustic Principle Pressure gradient Directional Pattern Cardioid Frequency range 20 Hz - 20 kHz Output impedance 100Ω Signal noise ratio 78 dB SPL (A - weighted per IEC651) Equivalent noise <16 dB SPL (A - weighted per IEC651) Maximum SPL 143dB SPL (@ 1kHz, 1% THD into 1KΩ load) Maximum output voltage +13.9dBu (@ 1kHz, 1% THD into 1KΩ load) Sensitivity -38 dB re 1 Volt/Pascal (12 mV @ 94 dB SPL) +/- 2 dB @ 1kHz Weight 101gm Dimensions 118mmH x 20mmW x 20mmD | 1 | 2 | 48 |  |  |  |
| 6.1.18.2x RODE SM3 (vibrāciju apsorbējošs) stiprinājums Shockmount vai ekvivalents līdzvērtīgs |  |  |  |  |  |
|  | cold shoe adaptor, for NTG-1, NTG-2, NT5, reduces vibration transmission to all shotgun thomann microphones, perfect for Rode NTG series, includes hot shoe adaptor for direct camera mounting. | 1 | 2 | 48 |  |  |  |
| 6.1.19.Lokanie Stereo plākstersavienojuma, jeb patch kabeļi vai ekvivalents līdzvērtīgs |  |  |  |  |  |
|  | 1/4" stereo TRS to 1/4" stereo TRS. Cable length: 5ft includes 6 cables |  |  |  |  |  |  |
| 6.1.20.Starpsavienojumu plākstersavienojumu panelis Neutrik NPPA-TT-S-FN vai ekvivalents līdzvērtīgs |  |  |  |  |  |
|  | Electrical Signal Type Digital suitability acc. AES/EBU (3.072 Mb/s and 6.144 Mb/s) Contact resistance 20 mΩ Dielectric strength 1 kVdc Frequencyrange DC to > 50 MHz Insulation resistance > 1 GΩ Channel separation > 100 dB @ 10 kHz, 600 terminated > 40 dB @ 6 MHz, 110 terminated Mechanical Insertion force < 10 N Withdrawal force > 8 N Lifetime > 5000 mating cycles Wiring Solder contacts Locking device Retention spring Material Contact plating TRIBOR® (0.2 µm AuCo over 2 µm NiP) (Jacks) Contacts Bronze (CuSn6) (Jacks) Shell Steel and aluminium Shell PA 66 blend (Jacks) Shell plating Black Environmental Solderability Complies with IEC 68-2-20 Temperature range -30 °C to +80 °C Optical Mobile Cables Dimensions 482 x 44 mm (19'' x 1U) Depth 178 mm (7'') Channels 2 x 48 jacks, full normalled, 288 solder terminals for fixed installations | 1 | 2 | 48 |  |  |  |
| 6.1.21.Mikrofona kabeļi 10m |  |  |  |  |  |
|  | Kabelis mikrofonam 10m | 1 |  |  |  |  |  |
| 6.1.21.1. 8 dzīslu stereo kanālu savienojumu kabeļi |  |  |  |  |  |
| 6.1.21.2.Enerģias pārveides (sintēzes) devējs Clark Synthesis TST429 Platinum vai analogs līdzvērtīgs |  |  |  |  |  |
|  | Continuous Power Handling:135 watts Impedance: 4 ohms Overload Protection: Polyswitch Frequency Response: 5Hz to 17kHz Electrical Connection: 3 ft.- 16 gauge, 2 wire Dimensions: 8 in. diam. x 2.25 in. high Magnet Assembly: 20 ounce Neodymium Iron Boride (MGO=38.9), Heat Transfer Fluid: Ferrofluidics To be compatible with other Clark Synthesis TST429 Transducers | 1 | 2 | 48 |  |  |  |
| 6.2.Skaņas aprīkojums un piederumi (projekts LV0086) |  |  |  |  |
| 6.2.1. M-S recording microphone kit: |  |  |  |  |  |  |
| 6.2.1.1. SENNHEISER MKH30P48 U3 (vai ekvivalents) |  |  |  |  |  |  |
|  | Figure-of-eight studio directional microphone with switchable pre-attenuation and switchable roll-off filter. Frequency response 40 - 20,000 Hz, sensitivity (free field, no load) 25 (8) mV/Pa ± 1 dB at 1 kHz, nominal impedance 150 Ohm, min. terminating impedance 1 kOhm, equivalent noise level A-weighted 13 (19) dB, CIR-weighted 22 (28) dB, max. SPL 134 (142) dB at 1 kHz, phantom powering 48 ± 4 V, supply current 2 mA, dimensions Ø 25 x 174 mm, weight approx. 110 g. Values in parentheses with attenuator switched on (–10 dB). Technical Data Transducer principle (Microphone) RF condenser microphone Pick-up pattern figure-of-eight Frequency response (microphone) 40.....20000 Hz Sensitivity in free field, no load (1kHz) 25 (8) mV/Pa +- 1 dB Nominal impedance 150 Ohm Min. terminating impedance 1000 Ohm Equivalent noise level 13 (19) dB Phantom Equivalent noise level weighted as per CCIR 468-3 22 (28) dB Maximum sound pressure level (passive) 134 (142) / 1 kHz Battery Specification 48 +- 4 V Phantom Current consumption 2 mA Dimensions d 25 x 174 | 1 | 2 | 48 |  |  |  |
| 6.2.1.2. SENNHEISER MKH40P48 (vai ekvivalents) |  |  |  |  |  |  |
|  | Pick-up pattern - cardioid Frequency response - 40 – 20,000 Hz Sensitivity (free field, no load, 1 kHz) 25 (8) mV/Pa ± 1dB Nominal impedance - 150 Ω Min. terminating impedance -1 kΩ Equivalent noise level A-weighted (DIN IEC 651)- 12 (18) dB CCIR-weighted (CCIR 468-3) - 21 (27) dB Max sound pressure level - 134 (142) dB at 1 kHz Power supply - phantom 48 ± 4 V Supply current - 2 mA Dimensions - Ø 25 x 153 mm Weight - approx. 100 g Values in parentheses with attenuator switched on (–10 dB) | 1 | 2 | 48 |  |  |  |
| 6.2.1.3. RYCOTE FULL WINDSHIELD KIT SUITABLE M-S RECORDING MICROPHONE KIT: MKH30P48 U3 & MKH40P48 MICROPHONES (vai ekvivalents) |  |  |  |  |  |  |
|  | Modular Suspension Windshield Windjammer™ Microphone Diameters: 19-25 mm, MKH and 30 mm Microphone Length (up to): from 120 mm up to 540 mm Maximum Wind-noise Attenuation: 35 dB | 1 | 2 | 48 |  |  |  |
| 6.2.2. Studio monitors Genelec 8050 A (vai ekvivalents) |  |  |  |  |  |  |
|  | Technical Specifications Input format Analog SPL Maximum short time sine wave acoustic output at 1 m on axis in half space, averaged from 100 Hz to 3 kHz ≥ 110 dB SPL Maximum peak acoustic output per pair with music material ≥ 120 dB SPL @ 1m Drivers Bass 8" Treble 1" metal dome Crossover frequencies 1.8 kHz Free field frequency response 38 Hz - 20 kHz Amplifier power /ch Bass 150 W Treble 120 W Speaker dimensions (H x W x D) mm 433 x 286 x 278 mm (Height with Iso-Pod™ 452 mm) Compatible in a system with existing Genelec 8050 A monitors and Subwoofer Genelec 7070 A (vai analogiem, ja tādi tiek piedāvāti) | 2 | 2 | 48 |  |  |  |
| 6.2.3. Subwoofer Genelec 7070 A (vai ekvivalents) |  |  |  |  |  |  |
|  | Maximum short term sine wave SPL output averaged from 30 to 85 Hz, measured in half space at 1 meter ≥112 dB SPL Input 6 main + LFE analog channels Sum out outputs 1 Driver 12" Free field frequency response 19 - 85 (120) Hz +/- 3 dB Manual acoustic controls Subwoofer level control +12 to -6 dBu (variable) Bass roll-off 0 to -6 dB (2 dB/step) Phase adjustment 0 to 270° (90°/step) @85 Hz Amplifier power 250 W Dimensions (H x W x D) mm 625 x 555 x 490 mm inches 24 5/8 x 21 7/8 x 19 5/16 Weight 50 kg (110 lb) Self generated noise level in free field @ 1 m on axis (A-weighted) ≤ 15 dB Harmonic distortion @ 95 dB at @ 1 m on axis in half space 30 ... 85 Hz 2nd ≤ 3 % 3rd ≤ 3 % Compatible in a system with existing Genelec 8050 A monitors and Subwoofer Genelec 7070 A (vai analogiem, ja tādi tiek piedāvāti) | 1 | 2 | 48 |  |  |  |
| 6.2.4.Power Amplifier THE T.AMP PROLINE 2700 (vai ekvivalents) |  |  |  |  |  |  |
|  | Professional power amp - 2x 1350W/4Ohms, 2x 900W/8Ohms, 2x 1600W/2Ohms, limiter, soft start, protection circuits, variable speed fan, ground switch, Dimensions: 482 x 480 x 132mm (19" rack/3U). Weight: 36 kg | 3 | 2 | 48 |  |  |  |
| 6.2.5. Recorder EDIROL R-44 (vai ekvivalents) |  |  |  |  |  |  |
|  | Data Type Format : WAV/BWF Sampling Bit Rate 16/24-bit Sampling Frequency 44.1kHz/48kHz/88.2kHz/96kHz/ Recording Media SDHC memory card (compatible with 64 MB - 8 GB) Analog Input Ch 1 - 4 : XLR/TRS Combo type, XLR type (phantom powered), TRS type (balanced/unbalanced), Analog Output Ch 1 - 4 : RCA Pin type (line output) Digital In/Out RCA Pin type (IEC 60958-3) Input Impedance XLR: 4k ohms or greater (balanced), TRS: 6k ohms or greater (balanced) Maximum Input +24 dBu (Input Sens Knob: +4 dBu) Output Impedance Line Output : 600 ohms Recommended Load Impedance Line : 4k ohms or greater Output Level Line Output : -20 dBu (fixed) Headphone : 40 mW + 40 mW Total Harmonic Distortion + Noise Line Output : 0.02 % (Input Sens : +4 dBu) Noise Level Line Output : -100 dBu (Input Sens : +4 dBu, Input Level : Center) Residual Noise Level Line Output : -103 dBu (Input Sens : +4 dBu, Input Level : Minimum) Frequency Response 20Hz - 40kHz(0/-3 dB) Dynamic Range AD : 100 dB DA : 104 dB Phantom Power: 48 V + or - 4 V, 8 mA per 1 channel (20 mA or less in all channels) | 1 | 2 | 48 |  |  |  |
| 6.2.6. M-audio MicroTrack2 (vai ekvivalents) |  |  |  |  |  |  |
|  | 2-channel WAV (BWF) and MP3 recording and playback for pro recording 1/8" Mic Input (A/D) Input Impedance 2.2K Ohms Maximum Input Level at minimum gain -3.6 dBV Channel-to-Channel Crosstalk <-95 dB SNR -101 dB, A-weighted Dynamic Range 101 dB, A-weighted THD+N 0.003% (-90 dB) Frequency Response 20 Hz to 20 kHz, +/- 0.5 dB Pre-amp Gain >52 dB stereo electret condenser power electret condenser power enabled 1/4" Mic/Line Inputs (A/D) Input Impedance >5.3K Ohms Maximum Input Level at minimum gain +4.3 dBu, balanced Channel-to-Channel Crosstalk <-95 dB SNR -101 dB, A-weighted Dynamic Range 101 dB, A-weighted THD+N 0.0027% (-91 dB) Frequency Response 20 Hz to 20 kHz, +/- 0.3 dB @ 48 kHz sample rate Pre-amp Gain >48dB Phantom Power +48V, Line Outputs (D/A) Output Impedance 465 Ohms Maximum Output Level +6 dBV, unbalanced Channel-to-Channel Crosstalk < -105 dB SNR -99 dB, A-weighted Dynamic Range 99 dB, A-weighted THD+N 0.0044 % (-87 dB) @ -1 dBFS, 1 kHz Frequency Response 20 Hz to 20 kHz, +/- 0.3 dB @ 48 kHz sample rate | 1 | 2 | 48 |  |  |  |
| 6.2.7. AKG K-271 MKII Studio Headphones (vai ekvivalents) |  |  |  |  |  |  |
|  | Professional stereo-studio-headphones for live sound and studio monitoring; Frequency range: 16–28.000 Hz; Sensitivity: 91 dB at 1 mW / 104 dBV; impedance: 55 ohms per channel; power handling capability: 200 mW; Type closed-back, dynamic headphones Sensitivity 91 dB/mW, 104 dB/V Frequency range 16 to 28,000 Hz Rated impedance 55 ohms Max. input power 200 mW Net weight (without cable) 240 g (8.5 oz.) | 2 | 2 | 48 |  |  |  |
| 6.2.8. MIDI controller AKAI MPD 18 (vai ekvivalents) |  |  |  |  |  |  |
|  | Mpc-style midi controller 16 pressure and velocity sensitive pads (genuine mpc pads) 3 switchable banks Mpc's 16-levels and full level features 16 configurable presets Assignable Q controller slider Midi out Usb out Powered via usb cable (or optional ac adaptor) | 1 | 2 | 48 |  |  |  |
| 6.2.9. Active monitors BEHRINGER MS40, pair (vai ekvivalents) |  |  |  |  |  |  |
|  | 24-Bit/192 kHz Digital 40-Watt Stereo Near Field Monitors 13#13 13213-13w13a13y13 13a13c13t13i13v13e13 13s13t13u13d13i13o13 13m13o13n13i13t13o13r13s13 13i13d13e13a13l13l13y13 13s13u13i13t13e13d13 13f13o13r13 13c13o13m13p13u13t13e13r13 13s13t13u13d13i13o13s13,13 13a13u13d13i13o13 13a13n13d13 13m13u13l13t13i13m13e13d13i13a13 13w13o13r13k13s13t13a13t13i13o13n13s13 13a13n13d13 13k13e13y13b13o13a13r13d13 13m13o13n13i13t13o13r13i13n13g13 13#13 13B13u13i13l13t13-13i13n13 13p13o13w13e13r13f13u13l13 13213 13x13 13213013-13W13a13t13t13 13a13m13p13l13i13f13i13e13r13s13 13w13i13t13h13 13i13m13m13e13n13s13e13 13h13e13a13d13r13o13o13m13 13#13 13P13o13w13e13r13f13u13l13 13w13o13o13f13e13r13s13 13a13n13d13 13h13i13g13h13-13r13e13s13o13l13u13t13i13o13n13 13t13w13e13e13t13e13r13s13 13p13r13o13v13i13d13e13 13a13n13 13u13l13t13r13a13-13l13i13n13e13a13r13 13f13r13e13q13u13e13n13c13y13 13r13e13s13p13o13n13s13e13 13#13 13U13l13t13r13a13-13h13i13g13h13 13r13e13s13o13l13u13t13i13o13n13 13213413-13b13i13t13/13113913213 13k13H13z13 13D13/13A13 13c13o13n13v13e13r13t13e13r13s13 13f13o13r13 13a13n13 13i13n13c13r13e13d13i13b13l13e13 13d13y13n13a13m13i13c13 13r13a13n13g13e13 13#13 13O13p13t13i13c13a13l13 13a13n13d13 13c13o13a13x13i13a13l13 13i13n13p13u13t13s13 13t13o13 13d13i13r13e13c13t13l13y13 13c13o13n13n13e13c13t13 13d13i13g13i13t13a13l13 13a13u13d13i13o13 13s13o13u13r13c13e13s13 13b13y13 13S13/13P13D13I13F13 13i13n13t13e13r13f13a13c13e13 13#13 13T13w13o13 13s13t13e13r13e13o13 13a13n13a13l13o13g13 13i13n13p13u13t13s13 13f13e13a13t13u13r13i13n13g13 13T13R13S13 13a13n13d13 13s13t13e13r13e13o13 13R13C13A13 13c13o13n13n13e13c13t13o13r13s13 13c13a13n13 13b13e13 13u13s13e13d13 13s13i13m13u13l13t13a13n13e13o13u13s13l13y13 13o13r13 13m13i13x13e13d13 13w13i13t13h13 13a13 13d13i13g13i13t13a13l13 13s13t13e13r13e13o13 13s13o13u13r13c13e13 | 1 | 2 | 48 |  |  |  |
| 6.2.10. Variable Function Generator (vai ekvivalents) |  |  |  |  |  |  |
|  | Instek GFG-8219A External Voltage Controlled Frequency (VCF) Function Duty cycle Controlled with Signal Inversion Capability Variable DC Offset Control Two-Step (-20dB x2) and Variable Attenuator Built in 6-digit counter INT/EXT counter function GCV output for synchronization Frequency Resolution: 0.1 Hz Waveforms (Sine, Square, etc.) Ramp, Sine, Square, Triangle Minimum Frequency 0.3 Hz Maximum Frequency, Sine wave 3 MHz Maximum Frequency, Square Wave 100 kHz Maximum Frequency, Triangle Wave 3 MHz Maximum Output Voltage 10 V Flatness 0.5 dB Modulation AM,FM Sweep Modes Linear,Log | 1 | 2 | 48 |  |  |  |
| 6.2.11. E-book reader Barnes & Noble nook (vai ekvivalents) |  |  |  |  |  |  |
|  | 13E13 13I13n13k V13i13z13p13l13e13x e13l13e13c13t13r13o13n13i13c13 paper display 6 inch Diagonal size, contrast with 16 level greyscale Weight: 317 grams 3.5 inch color touchscreen LCD. Wi-Fi ( 802.11 b/g) 2GB MP3 player Supported Formats: EPUB and eReader Formats, PDF, MP3s | 1 | 2 | 48 |  |  |  |
| 6.2.12. The Sssnake SK369S-15 stereo patch cables (vai ekvivalents) |  |  |  |  |  |  |
|  | 1/4" stereo TRS to 1/4" stereo TRS. Cable length: 5ft includes 6 cables | 4 | 2 | 48 |  |  |  |
| 6.2.13. Neutrik NYS-SPP-L1 patch panel (vai ekvivalents) |  |  |  |  |  |  |
|  | 1/4" modular Patch Panel with 2 rows of jack sockets 2x 24 (stereo/balanced/half-normalized) Signal Type AES/EBU Signals (digital) Contact resistance < 10 mΩ Dielectric strength 1 kVdc Frequencyrange DC to > 50 MHz Insulation resistance > 1 GΩ @ 500 V dc Channel separation > 100 dB @ 10 kHz, 600 terminated > 40 dB @ 6 MHz, 110 terminated Handles Phantom Power Yes | 1 | 2 | 48 |  |  |  |
| 6.2.14. Analogue oscilloscope DC to 35 MHz, HM 303-6 (vai ekvivalents) |  |  |  |  |  |  |
|  | Two channels Built-in calibrator for probe calibration Vertical deflection operating modes : Channel I or II singly, channel I and channel II alternately or chopper Sum or difference of : C I and C II Invert : K II XY mode : Channel I (X) and channel II (Y) Frequency range : 2 x DC up to 35 MHz (-3 dB) Rise time : <10 ns Deflection coefficients : 5 mV...20 V/cm @ 12 positions Input impedance : 1 MW @ 20 pF Maximum input voltage : 400 V (DC + peak AC) Active TV-Sync separator : Positive and negative Horizontal deflection time coefficients : 0.2 s/cm...0.1 µs/cm @ 20 positions X expansion : x 10: Up to 10 ns/cm Supply : 100...240 V @ 50/60 Hz Protection class : Protective class I (IEC1010-1/VDE 0411) Weight : 5,4 kg Dimensions : 380 x 285 x 125 mm | 1 | 2 | 48 |  |  |  |
| 6.2.15. Soundcard MOTU TRAVELER MKIII (vai ekvivalents) |  |  |  |  |  |  |
|  | Four 24-bit 192 kHz mic/guitar inputs A-weighted dynamic range 120dB THD+N of 0.00056% (-106dB) Compact size (14.75 x 9 inches) Powered via FireWire, Optional battery power via standard field battery pack (sold separately) 28 inputs / 30 outputs (at 44.1/48 kHz) Four combo jacks provide hi-Z 1/4" guitar input or low-Z XLR mic input with phantom power and pad, Clip protection - Up to +12 dB over zero, Individual 48V phantom power on each mic input Four 24-bit 192kHz analog inputs and eight analog outputs on balanced/unbalanced 1/4" TRS jacks optical I/O - 16 channels of ADAT lightpipe, 8 channels of SMUX (96 kHz) or two pairs of stereo TOSLink. Eight 24-bit 192kHz outputs on balanced/unbalanced 1/4" TRS jacks. Stereo 24-bit 96kHz AES/EBU in/out Stereo 24-bit 96kHz S/PDIF in/out Word clock in and out Built-in SMPTE time code sync - resolves to and generates time code | 1 | 2 | 48 |  |  |  |
| 6.2.16. Lab power supply13 HY3010 MASTECH (vai ekvivalents) |  |  |  |  |  |  |
|  | DC Power Supply 0-30 VDC/0-10 AMP13 Ieejošais spriegums: 110/220V±10%AC Izejas spriegums: 0~30V Izejas strāva: 0~10A Tīkla stabilitāte: ≤0.02%±3mV Slodzes stabilitāte: ≤0.01%±10mV Trokšņi un svārstības: ≤3mVrms | 1 | 2 | 48 |  |  |  |
| 6.2.17. Behringer BCF2000-WH (vai ekvivalents) |  |  |  |  |  |  |
|  | MIDI faders  Unique, total recall cascadable desktop MIDI controller with analog feel and an intuitive user interface  8 ultra-precise 100-mm motorized faders for ultimate control of virtual mixers, organ-drawbars (inverse mode) or virtual synths and samplers  4 virtual groups with 8 dual-mode, high-resolution encoders that feature LED rings and an additional push function  16 + 4 illuminated buttons freely assignable to all types of MIDI functions from note on/off, control change and program change to MMC and system exclusive data  All panel elements freely assignable—manually or via user-friendly learn mode  Additional multi-function foot switch and foot controller connectors can be used to address all types of MIDI data  32 user presets each with 4 encoder groups  Configurable MIDI and USB modes for ultra-flexible system integration  1 MIDI In plus 2 MIDI Outs, usable as an additional USB to MIDI interface  Multi-function 4-digit LED display with real-time parameter indication plus write-in fields for your own labeling | 1 | 2 | 48 |  |  |  |
| 6.2.18. HSS-HSS450 Hyper Sonic Sound Technology directional loudspeaker (vai ekvivalents |  |  |  |  |  |  |
|  | Audio Frequency response - 500Hz - 16 KHz Max. input tension for max. Output - 1.0V p-p each channel at 1KHz Buttons Equalizer - Switch 3 positions Connectors Audio input - 2 RCA/Cin ch Indicators Signal/saturation presence indicator Alimentation - External tension transformer 48VDC Maximal consumption - 100 W max Enclosure - Black ABS plastic Dimensions (enclosure) - 311,1 x 88,1 x 151,4 mm (LxPxH) Weight - 1,0 kg POWER REQUIREMENTS: Wattage - 100 watts maximum ELECTRICAL RATINGS: Input - 90V – 264VAC Universal Power Supply - 48V ~ 60Hz Output - 48V DC @ 2 Amps maximum MECHANICAL: Physical Dimensions - Depth (Front to Back); Height (Top-Bottom); Width (Left-Right) H450 - 88.1mm (3.47”) x 151.4mm (5.96”) x 311.1mm (12.25”) SHIPPING WEIGHT (Approximate): H450 - TBD ENVIRONMENTAL: Operating Temperature - 0°C to 40°C (32°F to 104°F) Storage Temperature -20°C to 50°C (-4°F to 122°F) Operating Humidity Range 0 to 95% (non-condensing ) Storage Humidity Range 0 to 95% (non-condensing) ULTRASONIC AND DSP PROCESSING: Carrier Frequency - Variable 40kHz – 50kHz Modulation Method - Proprietary Dynamic Carrier ULTRASONIC EMITTER: Type: ATC proprietary PVDF Piezo Film device AUDIO: Impedence - 10k Input Connector - 2 RCA style connectors System Configuration - Monaural (2 input channels summed together on the RCA connectors) Max Input for Max Output - 1.0Vp-p, each channel @ 1kHz SYSTEM: Frequency Resp onse - See Chart Max Audio SPL output - See Chart POWER AMPLICATION: Amplifier Type - Class D full bridge Amplifier Power Output Potential - 80W | 2 | 2 | 48 |  |  |  |
|  | KOPĀ |  |
|  | 22%PVN |  |
|  | Pavisam kopā |  |

* ja piedāvājuma parametri sakrīt ar pieprasījuma parametriem, atzīmēt ar X, ja parametri atšķirīgi, norādīt precīzu informāciju

**-Ietverot iekārtu piegādes izmaksas, iekārtu uzstādīšanas izmaksas un lietotāja pamata apmācības izmaksas.