7.pielikums

Atklāta konkursa

Nr. LiepU 2011/1 nolikumam

SPECIFIKĀCIJA - PIEDĀVĀJUMS

5.daļa Video aparatūra, aprīkojums un materiāli

(projekts LV0063)

| N.p.k. | Specifikācija | Skaits | Garantijas laiks (gadi) | Bojājuma novēršanas laiks (stundās) | Pretendenta piedāvājums* | Vienības izmaksas** LVL | Kopējā summa LVL |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 5.1.Soma kamerai CamBag Single I |  |  |  |  |  |
| Material Exterior: 1000 denier Cordura (PVC coated on inside) Material Interior: Padded Exterior Dimensions: 55 x 24 x 25cm (21.7 x 9.5 x 9.8") (LxWxH) Interior Dimensions: 52 x 16 x 22cm (20.5 x 6.3 x 8.7") (LxWxH) Carrying Options: 2 x Carry straps; 1 x Removable Padded Shoulder strap Weight: 2.5kg (5.51 lbs) Camera bag designed to fit camcorders up to 52cm (20.5") (DSR - HVR A1E; HDR-FX 1; HVR - Z1E; DSR-PD170P) | 4 | 2 | 48 |  |  |  |
| 5.2.Kameras ārējais mikrofons SONY ECM-673 Short Shotgun Microphone vai ekvivalents |  |  |  |  |  |
| Capsule Type : Electret condenser Connector: XLR-3 Cable Length: XLR-3 to XLR-3 Power Requirements : DC 40 to 52 V S/N Ratio : 77 dB or more (IEC179 A-weighted, 1 kHz, 1Pa) Sensitivity : -36 dB*1 +/-3 dB Directivity : Uni-directional (super-cardioid) Frequency Response : 40 Hz to 20 kHz Dynamic Range : 107 dB or more Induction Noise from External Magnetic Field : 0 dB SPL or less Wind Noise : 45 dB SPL or less (with windscreen), 50 dB SPL*2 (without windscreen) Inherent Noise (0dB=20uPa) : 17 dB SPL or less Max SPL (dB SPL)(0dB=20uP) : 124 dB SPL Output Impedance at 1kHz (Balanced) (1/2 +/- 20%) : 220 Omh +/-20% Dimensions : 20 x 200 mm Weight : Approx. 4.76 oz (135 g) | 1 | 2 | 48 |  |  |  |
| 5.3.Statīvi kamerām STATUS PRO K550 vai ekvivalenti |  |  |  |  |  |
| Single stage system Fluid head H550 - handle - 3 tube 1 stage DV tripod T621 - mid-level spreader S708 - rubber feet A857 Load Capacity 5kg Maximum Height 162cm Maximum Height w/o Column Extended N/A Minimum Height 51cm Folded Length 74cm Leveling Bubble/Illuminated: Yes/Yes Weight 4.5kg Counter Balance System 3 Steps + 0 Quick Release/Wedge Plate: Yes Balance Plate: Yes Tilt Drag Continuously variable fluid Tilt Range -90 to +85° Tilt Lock Yes Pan Drag Continuously variable fluid Pan Range 360° Pan Lock Yes Leg Material Aluminum alloy Head Attachment Fitting 75mm Leg Stages/Sections 2/3 Leg Lock Type Fast-action clamp Independent Leg Spread Yes Spiked/Retractable Feet Rubber Feet Center Brace Mid-level Komplektācijā soma statīvam | 2 | 2 | 48 |  |  |  |
| 5.4.Austiņas kamerām Sennheiser HD-280PRO vai ekvivalents |  |  |  |  |  |
| Transducer principle: dynamic, closed Nominal impedance: 64 Ohm Sound pressure level (SPL): 102 dB (IEC 268-7) Load rating: 500 mW THD, total harmonic distortion: 0,1 % Ear coupling: circumaural Contact pressure: 6 N Weight w/o cable: 220 g Jack plug: 3,5 / 6,3 mm stereo Connection cable: Coiled cable (min1m/max 3m) Frequency response (headphones): 8.....25000 Hz | 4 | 2 | 48 |  |  |  |
| 5.5.Radio mikrofoni Sennheiser EW100 ENG 2 vai ekvivalents |  |  |  |  |  |
| Type: Lavalier Microphone Technology: Electret condenser Microphone Operation Mode: Mono Connectivity Technology: Wireless – Radio Pick-up pattern: Omni-directional Response Bandwidth: -17960.0 Hz Signal-To-Noise Ratio: 110.0 dB Total Harmonic Distortion (THD): 0.9 % Max Sound Pressure: 130.0 dB Radio Transmitter Power: 30.0 mW Radio Frequency Range: 786 - 822MHz , 518 - 554MHz , 626 - 662MHz , 830 - 866MHz , 740 - 776MHz Radio Channel Qty: 4.0 Connector Type: 1.0 x Microphone ( Mini-phone 3.5 mm ) Included Accessories: Transmitter unit , Receiver unit Power Device: Power adapter - External Power supply: 2 x 1.5 V battery AA (Mignon) RF output power: 30 mW Operating time (transmitter): > 8 h Input voltage range: Mic/Line: 1,8V/2,4V (SK100G2), Mic:1,2V (SKP100G2) Included Qty: 6.0 Dimensions (Receiver): 82 x 64 x 24 mm Weight (Receiver): 158 g Dimensions (Transmitter): 82 x 64 x 24 mm (SK100 G2), 105x43x43mm (SKP100G2) Weight (Transmitter): 158 g (SK100G2), 195g (SKP100G2) Komplektācijā: 1 portable receiver; 1 bodypack transmitter; 1 clip-on microphone (omnidirectional pick-up pattern); 1 plug-on transmitter; 1 jack cable; 1 XLR cable; 1 camera adaptor; 6 AA batteries; 1 bag; Operating instructions | 2 | 2 | 48 |  |  |  |
| 5.6.Boom mikrofoni Sennheiser MKH 416 vai ekvivalenti |  |  |  |  |  |
| Transducer principle (Microphone): RF condenser microphone Pick-up pattern: super-cardioid/lobar Frequency response (microphone): 40.....20000 Hz Sensitivity in free field, no load (1kHz): 25 mV/Pa +- 1 dB Nominal impedance: 25 Ohm Min. terminating impedance: 800 Ohm Equivalent noise level: 13 dB Equivalent noise level weighted as per CCIR 468-3: 24 dB Maximum sound pressure level (passiv):130 dBVoltage48 +- 4 V PhantomCurrent consumption: 2 mA Phantom Powering: 48 ± 12 V Supply Current: 2 mA Dimensions: 19 x 250 mm Weight Approx.: 165 g. Windshield Kit: Dimensions 450mm L x 100mm Dia, Kit weight 1.45kg Komplektācijā: Mic case (includes foam windshield and stand mount); wind shield; wind jammer; suspension mount and pistol grip + screw driver; 1/2m XLR cable; 2 x 5m XLR Cable; boom pole; Phantom power box | 3 | 2 | 48 |  |  |  |
| 5.7.Apgaismojuma komplekts Kino Flo KIT-4804B-S120 vai ekvivalenti |  |  |  |  |  |
| 4ft 4Bank Select Kit, 120VAC Dimensions: 53.5 x 7 x 18.5” (136 x 18 x 46cm) Weight: 26 lb (12kg) Contents:?1 4ft 4Bank Fixture?1 4Bank Select Ballast ?1 MTP-BL41 Mount w/ Baby Receiver (16mm)?1 Extension, 25ft (Europlug)?1 Lamp Case?1 Soft Case 4 lamps 488-K32-S 4 lamps 488-K55-S 1 Stand (Folded Length ~40""; Max. Height ~10.5') 2 Grip Heads compatible with stand 1 Grip Arm 40"" compatible with Grip Head Fixture Specifications: Part Number: CFX-4804 Dimensions: 52 x 13 x 3.5"" w/6.5"" barndoors (132 x 33 x 9cm w/16.5cm barndoors) Weight w/Lamps: 11.5lb / 5.2Kg Lamps 4 Lamp Type: F75 / T12 Ballast Specifications: Part Number: BAL-450-120 Input Voltage: 120VAC 50/60Hz Output Frequency: 25kHz Amperage: F75/4.6A?F40/3.2A,F30/2.5A Lamp Switching: 4~1/Off Output Switching: 4ft/2ft Size: 12.5 x 12.5 x 2.5"" (32 x 32 x 6.5cm) Weight: 6.5lb (2.9Kg) 4 Lamps Safety Coated Part Number: 488-K32-S Description: 4ft Kino 800ma KF32 SFC Type: F75/T12/HO Length: 48” (1200mm) Diameter: 1.5” (38mm) Nominal Base: G13 Med Bipin Wattage: 75 Lumens: 3350 4 Lamps Safety Coated Part Number: 488-K55-S Description: 4ft Kino 800ma KF55 SFC Type: F75/T12/HO Length: 48” (1200mm) Diameter: 1.5” (38mm) Nominal Base: G13 Med Bipin Wattage: 75 Lumens: 3290 | 2 | 2 | 48 |  |  |  |
| 5.8.Prožektoru komplekts K3x650S Standard 650 W Tungsten Kit vai ekvivalents |  |  |  |  |  |
| 3 Light head 650 W (light heads can be used with 650W, 500W or 300W halogen lamps) 3 Filter holder 3 Barn door 3 Light shield ring 3 Graduated glass filter 3 Scrim kit 3 Scrim pouch 3 Stand 3 Stand bag 6 Lamp 650 W 1 Hard case Weight: 31.4 kg (69.2 lb.) Size: 105 x 53 x 31 cm (41.3 x 21 x 12.3”) | 2 | 2 | 48 |  |  |  |
| 5.9.Atstarotāji ar statīvu Walimex Reflector Panel 70x100cm + WT-803 Stand vai ekvivalents |  |  |  |  |  |
| Reflectorpanel Dimensions (WxH): approx. 70x100cm Weight: approx. 850g Connection: 5/8 inch Material: aluminium, synthetic fibre Colors: Silver/White Tripod Max. Height: approx. 200cm Min. Height: approx. 71cm Carrying length: approx. 71cm Max. load capacity: approx. 2,5kg Weight: approx. 760g Connection: 5/8 inch spigot with 1/4 and 3/8 inch thread Material: aluminium, plastic (fasteners) incl. convenient carrying bag | 3 | 2 | 48 |  |  |  |
| 5.10.Zaļais ekrāns Chroma Key Green Muslin Backdrop with a stand vai ekvivalents |  |  |  |  |  |
| Chroma key Backdrop: Size : 3 m x 6.3 m Color: Green Backdrop Stand: The side tripods are made of steel tubing with ?polyamide riser locks. The 4-segment cross-bar is of 25.4 mm dia.aluminum ?tubing. Height: 278 cm Width: 330 cm Net weight: 12 lbs | 1 | 2 | 48 |  |  |  |
| 5.11.CRT monitors DT-V100CG + HDLink vai ekvivalents |  |  |  |  |  |
| Type: Multi-format Monitor (16:9/4:3 switchable) Color Systems: NTSC, PAL; 1080/60i, 1080/59.94i, 1080/50i, 1080/24psF, 1080/23.98psF, 720/60p, 720/59.94p, 720/50p, 480/59.94i, 576/50i CRT: 10" (9" v) measured diagonally Scanning Frequency: H : 15 kHz, V : 50 Hz/60 Hz Horizontal Resolution: SD: 300 TV lines, HD: 230 TV lines Power Requirements: 120 V/220-240 V AC, 50 Hz/60 Hz Power Consumption: 0.9 A (120 V AC)/0.6 A (220-240 V AC) Color Temperature: 6,500°K / 9,300°K selectable Composite Signal: VIDEO A / VIDEO B: 2 lines, BNC connector x 4 (1 Vp-p, 75&) External Synchronized: EXT. SYNC: 1 line, BNC connector x 2 (0.3 Vp-p – 4 Vp-p, 75&) INPUT A/B: NTSC (3.58 MHz), PAL (4.43 MHz), B/W (50 Hz/60 Hz) INPUT C/D: Varies depending on the optional input unit RS-485: Serial connection, 1 line, RJ-45 connector (8-pin) x 2, compliant to RS-485 MAKE/TRIGGER: Point-of-contact connection, 1 line, RJ-45 connector (8-pin) x 1 Dimensions: W x H x D: 222 x 220 x 319.3mm Weight (Without Wide Mask and an input unit): 7.1 kg Connection cables included LCD monitoring converter: SDI Video Input: 2 x BNC inputs switch between SD-SDI, HD-SDI 4:2:2, HD-SDI 4:4:4, 2K via SDI and dual-link HD-SDI 4:4:4. SDI Video Output: 1 x BNC active loop through output switches between SD, HD 4:2:2, HD 4:4:4 and 2K. Optical Fiber Video Input: None Optical Fiber Video Output: None Multi Rate SDI Support: 270 Mb/s standard definition, 1.5 Gb/s high definition 4:2:2, 3 Gb/s 4:4:4 high definition and 2K film. Analog Audio Output: 6 x unbalanced 24 bit analog outputs on RCA connectors -10dB, de-embedded from SDI input. DVI-D Video Output: Supports SD, HD and 2K using Dual Link DVI-D displays up to 30 inches 2560 x 1600 in size. DVI-D Audio Output: DVI-D supports video only. Use RCA analog audio outputs for audio monitoring. HDMI Video Output: Via DVI-D to HDMI adaptor. Supports HDMI displays, such as a TV or video projector, up to 1920 x 1080 resolution. HDMI Audio Output: Via DVI-D to HDMI adaptor. HDMI Connection: Via included DVI-D male to HDMI Type A female adaptor. Updates and Configuration: USB 2.0 High Speed (480Mb/s) interface. 2K Format Support ?via DVI-D: 2048 x 1556p23.98, 2048 x 1556p24 and 2048 x 1556p25. HD Format Support ?via DVI-D: 720p50, 720p59.94, 720p60, 1080p23.98, 1080p24, 1080i50, 1080i59.94, 1080i60, 1080p50, 1080p59.94, 1080p60. HD Format Support ?via HDMI: 720p50, 720p59.94, 720p60, 1080p23.98, 1080p24, 1080i50, 1080i59.94 and 1080i60 , 1080p50, 1080p59.94 and 1080p60. SD Format Support ?via DVI-D: 625/25 PAL and 525/29.97 NTSC. SD Format Support ?via HDMI: 625/25 PAL and 525/29.97 NTSC. SDI Compliance: SDI Compliance: SMPTE 259M, SMPTE 274M, SMPTE 292M, SMPTE 296M, SMPTE 425M-B, ITU-R BT.656, ITU-R BT.601 and SMPTE 297M for Optical Fiber SDI. SDI Video Sampling: 4:2:2 and 4:4:4. SDI Color Precision: 4:2:2 10 bit and 4:4:4 10 bit SDI Color Space: 4:2:2 YUV, 4:4:4 YUV and 4:4:4 RGB. SDI Audio Sampling: Television standard sample rate of 48 kHz and 24 bit. DVI-D Configuration: Automatic adjustment using VESA E-EDID1.3. DVI-D Resolution: Pixel-for-pixel display on LCD displays. HDMI Configuration: HDMI automatically configures to connected display. HDMI Resolution: Pixel for pixel HD resolution input to connected device. Software Control: HDLink Utility included free for Windows XP, Windows Vista, Windows7 and Mac OS X. Gamma Correction: Independently adjustable 3D lookup tables per color component. Interactive real time adjustment of lookup tables. Firmware Upgrade: Automatically when new HDLink Utility is installed. Real Time Processing: Adaptive pull-down processor guarantees smooth motion display. Video Scaling via DVI-D: Pixel for pixel display. Scale up SD to fill display in 2D modes. Scale up HD to fill display in 2D modes. Installation: Small brick style compact design. Power Supply: 12 Volt universal power supply included. IEC (Europlug) power cable required. Cables and adapters included 3 gadu garantija | 1 | 2 | 48 |  |  |  |
| 5.12.Video plate Edirol V4 vai ekvivalents |  |  |  |  |  |
| Video Format: NTSC or PAL (ITU601) Video Sampling Rate: 13.5MHz, 4:2:2(Y:B-Y:R-Y), 8-bit, Frame synchronizer x 2 Video Input: S-Video: 4-pin mini DIN type Video (composite): RCA pin type x 4 (inputs 1-4; however if S-Video is simultaneously input to 1/2, S-Video takes priority) Video Output: S-Video: 4-pin mini DIN type x 1 Video (composite): RCA pin type x 2 Output level and Impedance: S-Video: 1Vp-p, 75ohm Video (composite): 1Vp-p, 75ohm Chrominance signal: 0.286mVp-p, 75ohm Transition Effects: Mix, Wipe: (4 types), Picture-in-Picture (4 types) Compositing Effects: Superimpose (remove black) Control MIDI: (in, out), V-LINK Power Supply: Dedicated AC Adaptor Current Consumption: 1500mA Size and Weight: Width 209 mm Depth 282 mm Height 77 mm Weight 1.8 kg Connection cables included | 1 | 2 | 48 |  |  |  |
| 5,13,Monitors filmēšanas laukumam Panasonic BT-LH1700WE17 + Flat Screen Monitor Case MO-LH1700 vai ekvivalents |  |  |  |  |  |
| Display Panel Panel Size: 17.1" Aspect Ratio: 15:9 Resolution: 1,280 x 768 pixel (WXGA) Display colors: More than 16,700,000 colors Contrast ratio 500:1 Brightness 300 cd/m2 Viewing Angle: 176° Operating Temperatur: +5 C - +35 C Operating Humidity: 20% - 80% (non dew) Storage Temperature: -20 C - +60 C Storage Humidity: 10% - 90% (non dew) Power requirements: AC100V - 240V 50/60Hz, DC12V (11V - 17V) Power consumption: 0.6 - 1.1A, 4A with 12V DC Dimensions (WxHxD): 430x309x81 mm / 17"x12.2"x3.2" (including stand: 430x323.5x198 mm / 17"x12.9"x7.9") Weight: 7.2 kg / 15.8 lbs (including stand: 8.1 kg / 17.8 lbs) Video : BNC x 2 (Through connector x 1) Y/C : 4-pin x 2 (Through connector x 1) Analog component (YPbPr/RGBS) : BNC x 8 SDI : BNC x 3 (switche-out connector x 1) Audio In (Pinjack x2) ? RS-232C interface GPI in (D-Sub 9-Pin) ? Tally (D-Sub 9-Pin) ? 12 V in (XLR, 4-pin) ? Power cord ?included Power cord hook included screw included Monitor Stand included User's manual included Connection cables included Monitor Case: Exterior: 1000 denier Cordura nylon Interior: Foam padding Exterior Dimensions 4.0 x 19 x 15" (10.16 x 48.26 x 38.1cm) (LxWxH) folded Interior Dimensions 17 x 12.9 x 7.9" (43.18 x 32.77 x 20.07cm) (WxHxD) Accommodates Panasonic BT-LH1700W or 1760W monitor Carrying/Transport Options Hand grip ?Shoulder strap Weight 4.7 lbs (2.13kg) | 1 | 2 | 48 |  |  |  |
| 5.14.Video recorder HVR-M15E vai ekvivalents |  |  |  |  |  |
| Recording Format: 1080/60i, 1080/50i, 480/60i (NTSC), 576/50i (PAL) Playout/down conversion format: 1080/60i, 1080/50i, 480/60i (NTSC), 576/50i (PAL), 480/60P, 576/50P Tape speed: HDV / DV SP : Max. 18.812 mm.s?DVCAM : Max. 28.218 mm/s Playback/recording time: HDV / DV SP:?- Max. 276 min with PHDV-276DM Cassette?- Max. 63 min with PHDVM-63DM Cassette?DVCAM :?- Max. 184 min with PHDV-276DM Cassette?- Max. 41 min with PHDVM-63DM Cassette Fast forward / rewind time: Approx. 2 min with PHDV-276DM cassette Input / output connectors / devices Video input/output: RCA pin x 2?Video Signal: 1 Vp-p, 75 ohm unbalanced, sync negative S-video input/output : Min-DIN 4-pin x 2?Y : 1 Vp-p, 75 ohm unbalanced, sync negative?C : 0.286 Vp-p (NTSC), 0.3 Vp-p (PAL), 75 ohm unbalanced Component video output : RCA pin x 3?Y : 1 Vp-p, (0.3V, sync negative)?Pr/Pb (Cr/Cb) : 700 mVp-p (100% color bar), input impedance 75 ohm i.LINK : 4-pin LANC : Stereo mini-jack (3.5mm) Audio Input : RCA pin x 2?Input level : -10 dBu, Input impedance: min. 10 kohm unbalanced?Max. input level : -16 dBu (approx. 5Vrms) in 60i mode, +21 dBu (approx. 4Vrms) in 50i mode Audio output : Output level : -10 dBu (full bit -20dB), impedance 47 ohm unbalanced in 60i mode, -10dBu (full bit -18dB), impedance 47 ohm, unbalanced in 50i mode?Impedance : Max. 1 kohm unbalanced Mass : Approx. 2.3kg (5 lb 1 oz) Power requirements : DC 8.4V Power Consumption : 8W (playback mode) Operating Temperature : 5 to 40 C (41 to 104 K) Storage Temperature : 120 to 60 C (-4 to 140K) Supplied Accessories : Remote Commander, AC adaptor, Power Cord, Stand, Size AA Batteries - 2pcs, Cleaning Cassette, Operating Instructions Connection cables included | 2 | 2 | 48 |  |  |  |
|  | KOPĀ |  |
|  | 22%PVN |  |
|  | Pavisam kopā |  |

* ja piedāvājuma parametri sakrīt ar pieprasījuma parametriem, atzīmēt ar X, ja parametri atšķirīgi, norādīt precīzu informāciju

**-Ietverot iekārtu piegādes izmaksas, iekārtu uzstādīšanas izmaksas un lietotāja pamata apmācības izmaksas.